## Slide 1: 2017 HackDay LED Kit
Arduino Moving Rainbow
Arduino Nano (CH340 driver)
1/2 breadboard (400 tie points)
330 ohm resistor
Red LED – max current 20ma
USB cable (mini-b)
60 pixel NeoPixel strip with GND (black), 5v (red) and data (yellow)
Momentary push buttons and wire
AAA battery pack
3 AAA batteries
Kit Contents
Download the Arduino IDE software from https://www.arduino.cc/en/Main/Software
Step 1: Download the Arduino Integrated Development Environment (IDE)
Step 2: Install the NeoPixel Library
Download CH341 driver from: http://www.wch.cn/download/CH341SER_ZIP.html (Chinese)
Step 3: Install the CH340 Driver
Step 5: Run the NeoPixel Example Strandtest
Step 6: Open the Moving Rainbow Labs
Open: http://moving-rainbow.readthedocs.io/en/latest/README/
Step 4: Set the Board to Nano and Port to /dev/cu.wchusbserial1420

## Slide 2: NeoPixel Code Examples
#include <Adafruit_NeoPixel.h>
#define LEDPIN 12 // connect the Data from the strip to this pin on the Arduino
#define NUMBER_PIXELS 60 // the number of pixels in your LED strip
Adafruit_NeoPixel strip = Adafruit_NeoPixel(NUMBER_PIXELS, LEDPIN, NEO_GRB + NEO_KHZ800);
Sample Preamble
void setup() {
strip.begin(); // initialize all the variables – don’t forget this line!
strip.setPixelColor(0, 255, 125, 0); // set pixel 0 to be yellow
strip.show(); // send the data to the LED strip – must do this after any change
delay(1000); // wait 1 second
}
Sample Setup
void loop() {
for (int i=0; i<NUMBER_PIXELS; i++) {
strip.setPixelColor(i, 255, 0, 0); // turn the "i"th pixel on
strip.show(); // send the data to the LED strip
delay(100); // wait 1/10th of a second – a lower number makes it go faster
strip.setPixelColor(i, 0, 0, 0); // turn the "i"th pixel off
}
}
Sample Moving Pixel
Learn how to solder solid wires to ends of battery pack
Hook up battery to breadboard rails
Hook up LED circuit in series with 330 ohm resistor
Add a button to turn on and off the LED
Plug in Arduino Nano to breadboard
Connect 5v and GND wires and verify the LEDs on Arduino work
Download Arduino IDE software and plug in USB cable
Get "blink" lab to work (configure board and port) and use upload button
Change the “delay” time in the blink lab from 10 to 1000 milliseconds
Download NeoPixel libraries
Connect NeoPixel strip to pin 12
Run NeoPixel example programs (strandtest)
Find Moving Rainbow examples
Work though various examples
On moving rainbow github/src find mini-maker-fair LED strip two buttons program
Wire button from D2 (interrupt) to ground
Try all the modes
Create your own mode pattern
Sample Labs