## Slide 1: 128x64 OLED Drawing Lab
Arduino Moving Rainbow
Arduino Nano with CH340 driver - $2.40
1/2 breadboard (400 tie points) - $1.20
USB cable (mini-b) - $1.20
128x64 OLED - $17
Kit Contents
Download the Arduino IDE software from https://www.arduino.cc/en/Main/Software
This guide assumes you have version 1.8.8 running
Step 1: Download the Arduino Integrated Development Environment (IDE)
Step 2: Install the u8g2 Library
Step 3: Find the U9g2 Page Buffer HelloWord Example
Step 4: Uncomment the SSD1306 128x64 unnamed Page Buffer 4-Wire Hardware SPI Constructor
// U8g2 Contructor List (Picture Loop Page Buffer)
U8G2_SSD1306_128X64_NONAME_1_4W_HW_SPI
#include <Arduino.h> #include <U8g2lib.h> #include <SPI.h> #include <Wire.h> U8G2_SSD1306_128X64_NONAME_1_4W_HW_SPI u8g2(U8G2_R0, 10, 9, 8); void setup(void) { u8g2.begin(); } void loop(void) { u8g2.firstPage(); do { u8g2.setFont(u8g2_font_ncenB10_tr); u8g2.drawStr(0,24,”CoderDojo Rocks!"); } while ( u8g2.nextPage() ); }

## Slide 2: u8g2 Code Examples
Sample Draw
Draw a circle
Draw a rectangle for the border
Update the center of the circle with the counter modulo the screen size
Get the circle to “bounce” off the edges of the screen
Sample Labs
drawStr(X, Y, "CoderDojo Rocks!")
drawFrame(x, y, width, height)
drawCircle(X, Y, radius, U8G2_DRAW_ALL)
drawDisc(X, Y, radius, U8G2_DRAW_ALL)
drawFilledEllipse(X,Y, height, width)
drawLine(x1, y1, x2, y2)
drawHLine(x, y, width)
drawVLine(x, y, height)
drawTriangle(x0, y0, x1, y1, x2, y2)
getDisplayWidth()
getDisplayHeight()
home()
Sample Drawing Functions
0
127 (x)
63 (y)
https://github.com/olikraus/u8g2/wiki/u8g2reference
drawBox(x, y, width, height)
drawEllipse(20,25, 10, 15, U8G2_DRAW_ALL))
u8g2.setFont(u8g2_font_unifont_t_symbols);
u8g2.drawGlyph(5, 20, 0x2603);
/* dec 9731/hex 2603 Snowman */
drawRBox(x, y, w, h, corner_radius)
https://github.com/dmccreary/coderdojo-robots/blob/master/docs/face-bot.md
Screen
Coordinates
FaceBot Example