## Slide 1: Oct 22nd, 2016 HackDay Kit Inventory
Arduino Nano (CH340)
1/2 breadboard (400 tie points)
330 Ohm Resistor
LED – max current 20ma
USB cable (mini-b)
12 pixel NeoPixel strip with GND (black), 5v (red) and data (yellow)
Momentary push button
3 AAA battery pack with switch
3 AAA batteries
Learn how to solder solid wires to ends of battery pack
Hook up battery to breadboard rails
Hook up LED circuit with 330 ohm resistor
Solder headers to Arduino Nano
Plug in Arduino Nano to breadboard
Connect 5v and GND wires and verify LEDs work
Download Arduino IDE software and plug in USB cable
Get "blink" lab to work (configure board and port) and use upload button
Download NeoPixel libraries from github
Place in Arduino libraries area
Connect NeoPixel strip to pin 12
Run NeoPixel example programs
Find Moving Rainbow examples
Work though various examples
On moving rainbow github/src find mini-maker-fair LED strip two buttons program
Wire button from D2 (interrupt) to ground
Try all the modes
Create your own mode
Sample Labs
Arduino Moving Rainbow