## Slide 1: Moving Rainbow Arduino Kit
Load Arduino software (IDE) on your PC or Mac1
Load "CH341SER" Arduino serial drivers2
Connect USB
Verify power LED is on
In IDE, set board to "Nano"
In IDE, select USB port
Load NeoPixel libraries from Sketch -> Include Libraries-> Manage Libraries
Run "StrandTest"
Load Moving Rainbow Tools
Try example patterns
Write your own color patterns!
Setup
http://moving-rainbow.readthedocs.io/en/latest/README/
Detailed Instructions
…or Google "Arduino Moving Rainbow"
Breadboard Layout
Circuit Diagram
https://www.arduino.cc/en/Main/Software
http://www.wch.cn/download/CH341SER_EXE.html
https://github.com/adafruit/Adafruit_NeoPixel
Window Device Manager
Solderless Breadboard

## Slide 2: Programming Arduino WS2811B (NeoPixel) LED Strips
Go To: https://github.com/adafruit/Adafruit_NeoPixel
Click the green "Clone or download" button and "Download ZIP"
Rename the file Adafruit_NeoPixel-master.zip to remove the "-master"
Uncompress the zip file (right click and look for the word "uncompress")
Place the file in your Home Arduino Libraries
Windows: C:\Users\dmccreary\My Documents\Arduino\libraries\Adafruit_NeoPixel
Mac: /Users/dmccreary/Documents/Arduino/libraries/Adafruit_NeoPixel
#include <Adafruit_NeoPixel.h>
#define LEDPIN 12 // connect the Data from the LED strip to this pin on the Arduino
#define NUMBER_PIXELS 12 // the number of pixels in your LED strip
Adafruit_NeoPixel strip = Adafruit_NeoPixel(NUMBER_PIXELS, LEDPIN, NEO_GRB + NEO_KHZ800);
Header
void loop() {
strip.setPixelColor(0, 255, 0, 0); // set pixel 0 to be red (index, r, g, b)
strip.show(); // send data to the strip
delay(1000); // wait one second
strip.setPixelColor(0, 0, 0, 0); // turn pixel 0 off
strip.show(); // send data to the strip
delay(1000); // wait a second
};
setup() void setup() {
pinMode(2, INPUT_PULLUP); // Pin 2 is pulled up to 5v when the switch is open
pinMode(3, INPUT_PULLUP); // Pin 3 is pulled up to 5v when the switch is open
strip.begin(); // sets up the memory for the LED strip
Serial.begin(9600);
Serial.println("Setup is done.");
}
Main Loop to Blink Pixel 0 to be Red
Setup
void loop() {
for (int i=0; i<strip.numPixels(); i++) {
strip.setPixelColor(i, 255, 165, 0); // set pixel i to be orange
strip.show();
delay(100);
strip.setPixelColor(i, 0, 0, 0); // turn pixel i off
strip.show();
delay(100);
}
}
Move Orange Pixel Down Strip
Use for loop to walk down the strip
"i" is the index or position on the strip
strip.numPixels() is the number of pixels
strip.setPixelColor(index, r, g, b)
is how we set a specific pixel's color
Getting NeoPixel Libraries from Github